## Slide 1: Evaluation environment for DCP MATLAB module

## Slide 2: Introduction
In the DCP project there are 4 Xilinx FPGAs that hold the signal processing module.
This module has to be evaluated before being instantiated into the design.
This document describes the evaluation system to make sure the module is operating as expected.

## Slide 3: The DCP MATLAB module
MATLAB DUT
AXIS
input
AXIS
output
configuration
D0
D1
D2
D3
D4
Dn
AXIS_DATA
AXIS_KEEP
AXIS_VALID
AXIS_READY
AXIS_LAST
D0
D1
D2
D3
D4
Dn
AXIS_DATA
AXIS_KEEP
AXIS_VALID
AXIS_READY
AXIS_LAST
The MATLAB module will have input and output buses, which will be in the AXIS bus protocol.
The module also will have a configure bus, to configure the module between modes of operation.

## Slide 4: The Evaluation environment
The Evaluation environment will have a system control (SC).
The SC will either be at the host computer or on-chip CPU.
The SC will get two inputs :
  Input data
  Expected results
The SC will control the module test:
  Config the module.
  Sent the input data for the test.
  Give a start command.
  Read the module output data and compare it to the expected results.
  Generate a PASS/FAIL message.
  Generate a log file to report the test results/errors.
MATLAB DUT
AXIS
input
AXIS
output
configuration
System Control
Input
Memory
Output
Memory
write
read
Input : Indata.c
Expected: Outdata.c
PASS/FAIL
Log.txt

## Slide 5
MATLAB DUT
AXIS
input
AXIS
output
configuration
Read
DMA
Write
DMA
DDR
PCIe

## Slide 6
MATLAB DUT
AXIS
input
AXIS
output
configuration
CPU
Read
DMA
Write
DMA
DDR
UDP